## Slide 1
Grow Food, Grow Strong · F-D2-01
1 / 19
DAY 2
Day 2 · Water
Make the rain walk, not run
✦
Storm on a slope
PICTURE · F-IMG-06
Notes: Opening circle: garden-map share in groups. Rotate roles.
Picture F-IMG-06 (coming) — Storm on a slope: A dark summer storm cloud over a rural homestead on a slope; rain curtains; brown water running along a path.

## Slide 2
POSTER F-P07
Grow Food, Grow Strong · F-D2-02
2 / 19
DAY 2
Where did the storm go?
■ Summer storms run away
■ They take our soil with them
▶ Play clip · flow-roof-rain.mp4
Notes: F-D2-S1. Ask where last summer's storm water went, and where it was in September.
Poster: F-P07
Clip F-ANI-07: public/course-animations/water-harvesting/flow-roof-rain.mp4

## Slide 3
Grow Food, Grow Strong · F-D2-03
3 / 19
YOUR TURN
Fast water, slow water
1
Pour on bare soil
2
Add stones and grass
3
Pour again
✦
Tray demo
PICTURE · F-IMG-07
Notes: Tray demo; every group's Materials person pours.
Picture F-IMG-07 (coming) — Tray demo: Two shallow trays of soil tilted on bricks: one bare with water running off carrying soil into a basin; one with a line of stones and grass where water spreads and soaks. Hands pouring from 2 L bottles.

## Slide 4
POSTER F-P07
Grow Food, Grow Strong · F-D2-04
4 / 19
DAY 2
Slow · Spread · Sink · Store
■ Slow it · spread it
■ Sink it · store it
✦
Artwork for F-P07 · Slow · Spread · Sink · Store
POSTER ART · F-P07-ART
Notes: Walk the homestead from roof to soil. Ask: what is the biggest tank on your land? (the soil)
Poster: F-P07
Also: F-ANI-08
Picture F-P07-ART (coming) — Artwork for F-P07 · Slow · Spread · Sink · Store: A homestead cross-section on a slope, left (top of slope) to right (bottom). Rain falls on a corrugated-iron roof → gutter → a first-flush pipe → a round covered tank with a tap and an overflow pipe → the overflow leads into a swale with a mound planted with small trees → below it mulched vegetable beds with a buried 2 ℓ bottle beside a plant → a washing basin tipped onto a mulched ring of banana-shaped plants (generic broad leaves) → a cut-away of soil at the bottom showing water soaking down into dark soil like a sponge. Four large soft numbered bands across the top (①②③④).
Clip F-ANI-08: public/course-animations/water-harvesting/watch-04-swale-infiltration.mp4

## Slide 5
Grow Food, Grow Strong · F-D2-05
5 / 19
YOUR TURN
Two catches on your map
1
Blue arrows: where water comes from
2
Two places to catch it
✦
My garden map
PICTURE · F-IMG-04
Notes: Groups help every person mark two water catches on their garden map.
Picture F-IMG-04 (coming) — My garden map: A hand-drawn map on paper seen from above: a house square, a north arrow, a tap, blue arrows of water, a sun symbol on the north side, a circle marking zone 1. Pencil and crayon style.

## Slide 6
Grow Food, Grow Strong · F-D2-06
6 / 19
DAY 2
Safety first
■ Tools point down
■ Nobody behind a swinging pick
■ Swap jobs every 10 minutes · drink water
✦
Tool safety
PICTURE · F-IMG-08
Notes: F-D2-S2. Say it before any tool is picked up.
Picture F-IMG-08 (coming) — Tool safety: A person carrying a spade and a pick with the points down; another person standing well to the side of someone swinging a mattock; a water bottle in the shade.

## Slide 7
POSTER F-P09
Grow Food, Grow Strong · F-D2-07
7 / 19
DAY 2
A swale on the level line
■ Ditch on the level line
■ Soil below as a mound
■ Safe spillway at the end
✦
Artwork for F-P09 · A swale on the level line
POSTER ART · F-P09-ART
Notes: Point to the five callouts. Not on steep slopes: use stone lines or grass strips there.
Poster: F-P09
Also: F-ANI-09
Picture F-P09-ART (coming) — Artwork for F-P09 · A swale on the level line: A large cross-section of a slope (uphill on the left). A trench on the level line (about 40 cm wide, 30 cm deep) with water standing in it and blue arrows soaking down and sideways under the mound; the dug soil forms a mound on the DOWNHILL side, mulched with grass and planted with a small tree and bushes whose roots reach towards the wet zone. Rain falls at the top; water runs down, stops in the ditch. A small inset (top right) of the swale from above following a curved line of pegs, with a stone-lined spillway at one end.
Clip F-ANI-09: public/course-animations/water-harvesting/watch-07-swale-overflow-pond.mp4

## Slide 8
POSTER F-P06
Grow Food, Grow Strong · F-D2-08
8 / 19
YOUR TURN
Mark the contour
1
One foot on the peg
2
Swing until the string hits the middle
3
Peg · move · repeat
▶ Play clip · flow-a-frame.mp4
Notes: Everyone in the group places the frame at least once. Smooth zig-zags; join sections.
Poster: F-P06
Clip F-ANI-06: public/course-animations/reading-landscape/flow-a-frame.mp4

## Slide 9
POSTER F-P09
Grow Food, Grow Strong · F-D2-09
9 / 19
YOUR TURN
Dig
1
Ditch above the pegs
2
Soil downhill
3
Keep the bottom flat
✦
Digging the swale
PICTURE · F-IMG-09
Notes: Roles: 2 dig, 1 rakes berm, 1 checks depth (30 cm), 1 fetches water and times swaps.
Poster: F-P09
Picture F-IMG-09 (coming) — Digging the swale: Five learners on a contour line of pegs: two digging the ditch uphill of the pegs, one raking soil into a mound downhill, one measuring depth with a marked stick, one bringing water.

## Slide 10
Grow Food, Grow Strong · F-D2-10
10 / 19
YOUR TURN
Test it
1
Two bottles of water in your section
2
Does it spread or run?
▶ Play clip · watch-07-swale-overflow-pond.mp4
Notes: If it runs to one end, take soil off the floor at the high end. Mulch the mound.
Clip F-ANI-09: public/course-animations/water-harvesting/watch-07-swale-overflow-pond.mp4

## Slide 11
POSTER F-P08
Grow Food, Grow Strong · F-D2-11
11 / 19
DAY 2
The magic rule
■ 1 mm of rain on 1 m² = 1 litre
✦
Artwork for F-P08 · How much rain from your roof?
POSTER ART · F-P08-ART
Notes: F-D2-S3. Hold up the 1 litre bottle. A 20 mm storm on 1 m² = one 20 litre bucket.
Poster: F-P08
Picture F-P08-ART (coming) — Artwork for F-P08 · How much rain from your roof?: Top: a single square metre of ground marked with four pegs and string, a rain cloud over it, and one 1-litre bottle beside it. Middle: a simple house with a corrugated roof, a measuring tape along the length and width at ground level, rain falling, and a row of identical 20 ℓ buckets lined up beside a tank. Bottom: a tank close-up — gutter with a gentle fall, a vertical first-flush pipe that fills before water reaches the tank, a lid, a tap raised on a stand above a bucket, and an overflow pipe leading to a planted swale.

## Slide 12
Grow Food, Grow Strong · F-D2-12
12 / 19
YOUR TURN
Measure the roof
1
Length × width on the ground
2
Never climb the roof
✦
Measuring the roof
PICTURE · F-IMG-11
Notes: Knotted string (knot every metre) or a tape.
Picture F-IMG-11 (coming) — Measuring the roof: Two learners stretching a knotted string along the ground under the edge of a corrugated-iron roof of a hall; a third counting knots.

## Slide 13
POSTER F-P08
Grow Food, Grow Strong · F-D2-13
13 / 19
DAY 2
How many buckets?
■ 10 m × 6 m = 60 m²
■ 60 × 20 mm × 0.8 = 960 litres
■ ≈ 48 buckets from one storm
✦
Buckets from one storm
PICTURE · F-IMG-12
Notes: Worked example, then the venue roof. Counters method: one bottle top = 1 m² = 1 bucket. Yearly: × your area's yearly rain (check locally).
Poster: F-P08
Picture F-IMG-12 (coming) — Buckets from one storm: A small house roof with rain and, beside it, a long neat line of identical 20 L buckets receding into the distance — many buckets.

## Slide 14
POSTER F-P08
Grow Food, Grow Strong · F-D2-14
14 / 19
DAY 2
Gutter, first-flush, tank
■ First rain washes the roof — let it go
■ Lid on · tap above a bucket
■ Overflow to the garden
▶
First-flush tank
CLIP · F-ANI-10
Notes: Each learner estimates their own roof and writes the storm number on their map.
Poster: F-P08
Clip F-ANI-10: public/course-media/farmer-5day/F-ANI-10.mp4
Picture F-ANI-10 (coming) — First-flush tank: Rain on a corrugated-iron roof. The first dirty water (leaves, dust) fills a vertical side pipe until it is full; then clean water flows past it into a covered round tank; the tank fills and the overflow pipe sends water to a planted swale. (Replaces the withdrawn clip `water-harvesting/watch-16-first-flush-tank.mp4`.)

## Slide 15
Grow Food, Grow Strong · F-D2-15
15 / 19
DAY 2
Every drop twice
Four stations · 10 minutes each
✦
Artwork for F-P07 · Slow · Spread · Sink · Store
POSTER ART · F-P07-ART
Notes: F-D2-S4 carousel: bottles, mulch, greywater, banana circle.
Picture F-P07-ART (coming) — Artwork for F-P07 · Slow · Spread · Sink · Store: A homestead cross-section on a slope, left (top of slope) to right (bottom). Rain falls on a corrugated-iron roof → gutter → a first-flush pipe → a round covered tank with a tap and an overflow pipe → the overflow leads into a swale with a mound planted with small trees → below it mulched vegetable beds with a buried 2 ℓ bottle beside a plant → a washing basin tipped onto a mulched ring of banana-shaped plants (generic broad leaves) → a cut-away of soil at the bottom showing water soaking down into dark soil like a sponge. Four large soft numbered bands across the top (①②③④).

## Slide 16
Grow Food, Grow Strong · F-D2-16
16 / 19
YOUR TURN
Bottle drip-waterer
1
Two small holes near the bottom
2
Bury to the neck beside the plant
3
Hot nail: pliers only
✦
Bottle drip-waterer
PICTURE · F-IMG-13
Notes: Station A.
Picture F-IMG-13 (coming) — Bottle drip-waterer: Cut-away of soil with a 2 L bottle buried to its neck beside a young plant; tiny droplets leaving two small holes near the base towards the roots.

## Slide 17
Grow Food, Grow Strong · F-D2-17
17 / 19
DAY 2
Mulch right
■ A hand's width deep
■ A fist's gap around stems
■ Halves the watering
▶ Play clip · flow-sheet-mulching.mp4
Notes: Station B. Dig and compare moisture under mulch and bare soil.
Clip F-ANI-12: public/course-animations/food-forest/flow-sheet-mulching.mp4

## Slide 18
POSTER F-P07
Grow Food, Grow Strong · F-D2-18
18 / 19
DAY 2
Greywater and the banana circle
■ Washing water to trees, not leaves you eat raw
■ Never toilet, nappy, bleach or oil water
■ Change where you pour
▶
Greywater to mulch
CLIP · F-ANI-11
Notes: Stations C and D. Mark a banana circle 1.5–2 m across; centre bowl filled with grass and prunings.
Poster: F-P07
Clip F-ANI-11: public/course-media/farmer-5day/F-ANI-11.mp4
Picture F-ANI-11 (coming) — Greywater to mulch: A person carries a basin of used washing water and pours it slowly onto a thick mulch ring around a broad-leaved banana-like plant and a fruit tree (never onto leafy vegetables); in cut-away the water soaks through the mulch down to the roots. (Replaces the withdrawn clip `water-harvesting/watch-21-greywater-mulch.mp4`.)

## Slide 19
Grow Food, Grow Strong · F-D2-19
19 / 19
DAY 2
Tonight
■ One bucket of washing water on a plant
■ Bring grass, leaves, greens, manure tomorrow
✦
Closing circle
PICTURE · F-IMG-05
Notes: Closing circle.
Picture F-IMG-05 (coming) — Closing circle: Late-afternoon warm light; a circle of standing people, one holding up a hand to speak; tools laid neatly on a tarp in the centre.